## Slide 1: Progress report CW8
Bachelor Thesis, Elias Hanelt, 2025

## Slide 2: How to organize
Using typst for my bachelor thesis and weekly progress reports
Created a github repo for the bachelor thesis

## Slide 3: Trying to build a prototype with the Arduino Portenta H7
Before starting the bachelor thesis, Giacomo and I picked the Portenta H7, Portenta Max Carrier, Portenta Breakout Board for developing a prototype
Next steps: Ordering a Mid Carrier board to access the pins
Developed a small prototype to test things out

## Slide 4: Creating a simple test script

## Slide 6: Errors while testing
Due to loose connections, testing was quite hard
-> ordering the mid size carrier

## Slide 7: Designing a PCB
Requirements:
  2 ADCs, 2 D/A converters for 2 BMC input/output pairs
  JTAG programmer to program the STM32H7x
  Ethernet Jack
  USB-C power supply / data transfer
  On/Off switch, physical knobs for gain/delay and threshold control
  Debug LEDs/Testpads
  Choosing parts that are available at JLCPCB for PCBA

## Slide 8: Choosing the right IC
STM32H7x series
  offers great adc performance (high resolution and sample rate)
  integrated 10/100 Mbps Ethernet MAC
  Dual core to handle communication and signal filtering at the same time
  Since we only need to 2 pairs of ADCs and D/A converters STM32H723vgt6 is enough

## Slide 9: Creating the schematics

## Slide 11: Choosing Rust over everything
Choosing rust as programming language because of its:
  Memory Safety & Reliability
  Zero-Cost Abstractions
  Async Concurrency with Embassy-rs
  Scalable & Maintainable Codebase

## Slide 12: Codebase setup
A bit tricky since rust embedded is quite new